## Slide 1
Equations of State for CO2 and CO2-Rich Mixtures
What is Relevant for Non-Ideal Compressible-Fluid Dynamics?
R. Span
3rd Int. Seminar on Non-Ideal Compressible-Fluid Dynamics for Propulsion & Power

## Slide 2
Overview
Why do we use Helmholtz equations of state?
What is special about thermodynamic properties of carbon dioxide?
Why do properties in the (extended) critical region require special attention?
Do we utilize the potential of Helmholtz equations of state properly?
Equations of state for carbon dioxide rich mixtures
How do impurities affect the properties of carbon dioxide?
Can we use mixtures to improve processes?

## Slide 3
Why do we use Helmholtz equations of state?
Hypothesis: The second law of thermodynamics yields a complete description of equilibrium states
A complete description of equilibrium states should be possible in terms of the independent variables introduced by the second law of thermodynamics
This approach results in …
closed systems:
flow processes:
Entropy cannot be measured directly, has an arbitrary reference state
Nobody wants an equation of state that uses entropy as variable

## Slide 4
Why do we use Helmholtz equations of state?
Legendre transformation allows for a loss free change of variables
Closed systems:
with the Helmholtz (free) energy
Flow processes:
with the Gibbs (free) enthalpy
In engineering calculations typical combinations of independent variables are
T,p  direct calc. from g(T,p), one dim. iteration from a(T,r) p,h  one dim. iteration from g(T,p), two dim. iteration from a(T,r) p,s  one dim. iteration from g(T,p), two dim. iteration from a(T,r)
g(T,p) seems to be the right choice for engineering applications!

## Slide 5
Why do we use Helmholtz equations of state?
For consistent calculations across phase boundaries, the fluid surface needs to be described by a single mathematical expression
Gibbs energy allows for fast calculations but does not allow for a closed description of the whole fluid surface
Pressure
Temperature
ps curve
liquid
saturated vapour
supercritical
saturated liquid
discontinuous plot of most properties
Density
Temperature
two phase region
saturated vapour
supercritical
saturated liquid
continuous plot becomes possible

## Slide 6
Why do we use Helmholtz equations of state?
Fundamental equations of state allow for a consistent calculation of all thermodynamic properties by combining derivatives
For the reduced Helmholtz energy we write:

## Slide 7
Why do we use Helmholtz equations of state?

## Slide 8
Why do we use Helmholtz equations of state?

## Slide 9
Why do we use Helmholtz equations of state?

## Slide 10
What is special about thermodynamic properties of carbon dioxide?
Carbon Dioxide
Nitrogen
R134a

## Slide 11
What is special about thermodynamic properties of carbon dioxide?
Carbon Dioxide
Critical temperature Tc = 304.1282 K (30.98° C)
Critical pressure pc = 7.3773 MPa
Critical density rc = 467.6 kg/m3
Triple point temperature Ttr = 216.592 K (-56.56° C)
Triple point pressure ptr = 0.51795 MPa
The critical region of CO2 is experimentally well accessible
CO2 was considered the reference fluid for critical phenomena in the 1980s / 1990s
A reference eq. of state that does not show nonanalytical behavior at the critical point would not have been accepted

## Slide 12
Why do properties in the critical region require special attention?
Theory tells that at the critical point…
the isochoric heat capacity cv gets infinite
the speed of sound w gets zero
Nonanalytical terms required in multiparameter equations of state

## Slide 13
Why do properties in the critical region require special attention?
Theory tells that at the critical point…
the isochoric heat capacity cv gets infinite
the speed of sound w gets zero
Nonanalytical terms required in multiparameter equations of state
infinite
infinite
nonanalytical

## Slide 14
Why do properties in the critical region require special attention?
Theory tells that at the critical point…
the isochoric heat capacity cv gets infinite
the speed of sound w gets zero
Nonanalytical terms required in multiparameter equations of state
infinite
infinite
nonanalytical
zero
infinite
nonanalytical

## Slide 15
Why do properties in the critical region require special attention?
Theory tells that at the critical point…
the isochoric heat capacity cv gets infinite
the speed of sound w gets zero
Nonanalytical terms required in multiparameter equations of state
infinite
infinite
nonanalytical
zero
infinite
nonanalytical
Nonanalytical terms in the Span & Wagner EOS (1996)

## Slide 16
Why do properties in the critical region require special attention?
Is nonanalytical behavior actually relevant for NICFD?

## Slide 17
Why do properties in the critical region require special attention?
Is nonanalytical behavior actually relevant for NICFD?
The contribution of derivatives of the pvT surface is dominant in the critical region
Make sure equations of state describe p(r,T) very well!

## Slide 18
Why do properties in the critical region require special attention?
Empirical multiparameter equations of state describe the pvT surface in the (extended) critical region more accurately then scaled equations of state
Carbon Dioxide

## Slide 19
Why do properties in the critical region require special attention?
Nitrogen
Empirical multiparameter equations of state describe the pvT surface in the (extended) critical region more accurately then scaled equations of state

## Slide 20
Do we utilize the potential of Helmholtz equations of state properly?
Of course, this depends on your algorithms / your code!
Just one example on how to mess things up …
ideal gas
=



real fluid

Some well known definitions have been derived for ideal gas, do not hold in combination with real fluids

## Slide 21
Do we utilize the potential of Helmholtz equations of state properly?
Some well known definitions have been derived for ideal gas, do not hold in combination with real fluids
To derive the temperature from k we need the ideal gas assumption
CO2

## Slide 22
Do we utilize the potential of Helmholtz equations of state properly?
Do we need the isentropic exponent k at all?
The enthalpy h2s = h(p2,s1) can be calculated directly from Helmholtz equations of state
So can T2s = T(p2,s1) or T2 = T(p2,h2)
Algorithms should be checked for obsolete routines!
Using enthalpy and entropy directly avoids problems with averaging of properties that change drastically for strongly non-ideal fluids (like cp or w)

## Slide 23
Equations of state for carbon dioxide rich mixtures
Helmholtz energy for mixtures
Ideal gas contribution
Reducing parameters as functions of composition
Reducing parameters correspond to critical parameters of pure fluids
Residual fluid contribution
Pure fluid contribution at corresponding states
Departure term
Approach by Lemmon and Tillner-Roth (1999)
(as discribed by Thol et al., 2019)

## Slide 24
Equations of state for carbon dioxide rich mixtures
Reducing parameters
Departure term
Combination of polynomial, exponential and special exponential terms
Adjustable parameters: coefficients, temperature and density exponents, exponential parameters, number of terms

## Slide 25
Equations of state for carbon dioxide rich mixtures
No experimental data available: Application of predictive combination rules such as the Lorentz-Berthelot or linear mixing rules
Few experimental data or only a single thermodynamic property type available: Adjustment of one or more binary interaction parameters
Experimental data for similar binary mixtures with adequate quality and quantity available: Development of generalized departure function and adjustment of weighting factor
Comprehensive database including many state points with known experimental uncertainty and different thermodynamic properties available: Development of binary-specific departure function

## Slide 26
Equations of state for carbon dioxide rich mixtures
 (d) highest accuracy
 (c) high accuracy
 (b) limited accuracy
}  (a) low accuracy
Herrig et al. (2018)
Herrig et al. (2018)

## Slide 27
How do impurities affect the properties of carbon dioxide?
Helmholtz models for mixtures allow for the same calculations as for pure fluids
Impurities have a strong impact in particular on the phase boundary
Properties in the (extended) critical region are strongly influenced as well

## Slide 28
How do impurities affect the properties of carbon dioxide?
Helmholtz models for mixtures allow for the same calculations as for pure fluids
Impurities have a strong impact in particular on the phase boundary
Properties in the (extended) critical region are strongly influenced as well

## Slide 29
Can we use mixtures to improve processes?
To calculate properties for mixtures is numerically more demanding than for pure fluids
Table look-up routines get more complicated, because the number of independent variables increases (composition vector)
However: Except for phase equilibrium calculations the composition remains constant; mixtures can be treated like pure fluids in table look-up
Optimization of processes for mixtures is a viable option!
Advantages may be expected for heat transfer processes due to a better fit of temperature curves (although supercritical heat supply is already pretty good …)

## Slide 30
Can we use mixtures to improve processes?

## Slide 31
Thank You For Your Patience – Do You Have Questions?
Why do we use Helmholtz equations of state?
What is special about thermodynamic properties of carbon dioxide?
Why do properties in the (extended) critical region require special attention?
Do we utilize the potential of Helmholtz equations of state properly?
Equations of state for carbon dioxide rich mixtures
How do impurities affect the properties of carbon dioxide?
Can we use mixtures to improve processes?